## Slide 1: Efficient Representation and Distribution of Video (and Related Media)
David Taubman
School of Electrical Engineering & Telecommunications The University of New South Wales Sydney, Australia
Note: If you reproduce any portion of this presentation,
quote the source according to the footer on each slide.

## Slide 2: Overview
Objectives – scalability, accessibility, efficiency, …
What can you do with JPEG2000? – interactivity!
On the way to scalable video – why is it so hard?
  motion compensated lifting – what does it solve?
  current scalable video standardization
  spatial scalability – promising directions
  motion modeling – beyond quad-trees
  orientation adaptive bases – beyond bandelets
Distribution of scalable media over lossy channels
Client/server systems with state
  the role of intelligent servers
  when embedding fails – disruptive refinement and D+R
  connections with distributed coding

## Slide 3: Objectives
Efficiency – small D+R, for  > 0 of your choice
  … of course!
  … but this is not everything

## Slide 4: Objectives
Accessibility – disjoint subsets of interest
  spatial region of interest
  temporal region (or individual frames) of interest
  Implications:
    need to break or localize dependencies

## Slide 5: Objectives
Scalability – degrees of interest
  resolution scalability
    spatial resolution (frame size)
    temporal resolution (frame rate)
  quality scalability
  Implications:
    want to embed coarser approximations within finer ones

## Slide 6: Other objectives
Robustness – to transmission errors
  generally facilitated by accessibility (decoupling) and scalability (embedding → prioritization)
Reversibility
  ability to recover original at sufficiently high bit-rate
    possibly with some purely numerical uncertainty
Low delay
  only for some applications
Complexity
  a moving target
  but, scalable complexity is nice

## Slide 7: JPEG2000 – more than compression
Decoupling and embedding
embedded code-block bit-streams
embedded code-block bit-streams
LL2
LH2
HH2
HL2
HL1
HH1
LH1

## Slide 8: JPEG2000 – more than compression
Spatial random access

## Slide 9: JPEG2000 – more than compression
Quality and resolution scalability
LL2
LH2
HH2
HL2
HL1
HH1
LH1
layer 1
layer 2
layer 3
quality layers

## Slide 10: JPEG2000 – dimensions of scalability
subset having low resolution, at very high quality
subset having moderate resolution, with coarse quantization
Res 0
Details for Res 1
Layer 1
Layer 2
Layer 3
resolution
Resolution Scalable Embedding
Quality Scalable Embedding
Resolution and Distortion Scalable Embedding
Details for Res 2
quality layers

## Slide 11: JPEG2000 – JPIP interactivity (IS15444-9)
Client sends “window requests”
  spatial region, resolution, components, …
Server sends “JPIP stream” messages
  self-describing, arbitrarily ordered
  pre-emptable, server optimized data stream
Server typically models client cache
  avoids redundant transmission
Cache Model
imagery
window request
JPIP Server
JPIP Client
Target (file or code-stream)
Decompress/render
Application
JPIP stream + response headers
Client Cache
window
window
status

## Slide 12: What can you do with JPIP?
Demo
  Demonstrates interactive remote browsing of a large 3D medical volume, compressed using a 3D wavelet transform, fully conforming to the JPEG2000 (Part 2) and JPIP standards (IS 15444-2 and IS15444-9).

## Slide 13: Scalable video – things that don’t work so well
3D wavelet transform – (Karlsson & Vetterli, ICASSP’88)
Temporal filtering ineffective with motion
  low-pass frames corrupted by “ghosting”
  poor energy compaction
0
x
1
x
2
x
3
x
1
H
L
s

1
HH
s

1
L
H
s

1
H
t

1
H
t

2
H
t

2
L
t

1
H
L
s

1
HH
s

1
L
H
s

1
H
L
s

1
HH
s

1
L
H
s


## Slide 14: Traditional video coding – MC DPCM
transform + quantize
dequantize + transform
MC
Decoder: modeled by encoder
MC
transform + quantize
dequantize + transform
MC
MC
MC
MC

## Slide 15: Traditional video coding – performance
Successive generations have seen marked performance improvements
  e.g., MPEG-2 @ 1 Mbit/s  H.263 @ 800 kbit/s  MPEG-4 @ 700 kbit/s  H.264/AVC @ 400 kbit/s
Explanations:
  more sophisticated motion modeling
    from 16x16 fixed size block motion
    to hierarchical (16x16, 16x8, 8x8, 8x4, 4x4) @ ¼ pel/vector
  careful use of R-D optimization
    directly optimize D+R over all macro-block modes
  multiple reference frames, directed intra prediction, …
Adapted from: (Sullivan & Wiegand, Proc. IEEE, Jan 2005)

## Slide 16: Traditional video coding – scalability??
Scalability implies many ways of decoding
  reduced spatial resolution  different transform
  reduced SNR (bit-rate)  different quantization
  reduced motion quality  different MC operators
Traditional MC DPCM approach relies on reproducing decoder state in the encoder
Various approaches considered:
  MPEG-2: partioning and layered coding of DCT coeffs
    differing encoder/decoder states  drift (noise propagation)
  MPEG-4 FGS: layered coding with state prediction
    encoder typically uses state of lowest quality decoder
  Theoretical analysis of inherent performance losses
    (Cook, Prades-Nesbot, Liu & Delp, IEEE Trans. IP, Aug 2006)

## Slide 17: Opening the loop – noise propagation
transform + quantize
dequantize + transform
MC
Decoder: modeled by encoder
MC
transform + quantize
dequantize + transform
MC
MC
MC
MC

## Slide 18: Open loop hierarchical prediction
AKA: UMCTF – with wavelet-based coding (van der Schaar and Turaga, ICASSP 2003)
  Limits propagation of quantization noise
AKA: Hierarchical B-frames – with DCT-based coding
Requires long base-line motion modeling!
0
1
2
3
4
0
2
4
0
4

## Slide 19: Why prediction alone is sub-optimal
0
0
1
even frames
odd frames
residual
forward transform
reverse transform
quantization
1
-½
-½
1
1
½
½
1
Redundant spanning of low-pass content by both channels 
High-pass quantization
noise has unnecessarily high energy gain.
Bi-directional prediction

## Slide 20: Reduced noise power through lifting
Pass –ve fraction of high band through low band synthesis path
  removes low freq. noise power from synthesized high band
Add compensating step in the forward transform
  does not affect energy compacting properties of prediction
even frames
odd frames
0
0
1

## Slide 21: Motion compensated lifting
MC warped lifting steps  xform is applied along motion trajectories:
  provided trajectories exist (motion model is invertible);
  strictly true only for spatially continuous frames (Secker & Taubman)
even frames
odd frames
MC
warp
MC
warp
MC
warp
MC
warp
Motion compensate each lifting step
  transform remains reversible
Proposed in 2001:
  (Pesquet-Popescu & Bottreau)
  (Secker & Taubman)
  (Luo, Li, Li, Zhuang, Zhang)

## Slide 22: Other temporal lifting transforms
Optimal update step for 5/3 transform
  (Girod, Han, Chang, PCS 2004)
A 7/5 transform with 3 temporal lifting steps
even
odd
low
high
0
0
1
Band energy gains:
  E0 = 0.38
  E1 = 0.72
Not so orthogonal
  |max|  0.16
even
odd
low
high
0
0
1
Band energy gains:
  E0 = 0.50
  E1 = 0.50
Virtually orthogonal
  |max|  0.01

## Slide 23: Other applications of MC lifting
Compression of volumes (CT, MRI, etc.)
  MC slice transform – (Taubman, Leung, Secker, ICIP’02)
Scalable lightfields (3D scenes)
  (Girod, Chang, Ramanathan & Zhu – ICASSP 2003)
  1D scanned or 2D separable MC interview transform
    apply MC lifting steps to views
  “Motion” field derived from surface geometry (proxy)
Scalable multiview video (4D scenes)
  (Garbas, Fecker, Troger & Kaup – MMSP 2006)
f2
f0
Surface geometry (proxy)
f1

## Slide 24: Geometry adaptive image compression
Reversible skew + DWT applied on blocks
  (Taubman and Zakhor – Trans IP, July 1994)
Reversible skew + bandletization applied on blocks
  (Bandelets: Le Pennec & Mallat – VCIP 2003)
shift rows
L2
H1
H2
Packet DWT
shift rows
DWT
LL
HL
LH
HH

## Slide 25: Geometry adaptive packet lifting
Fixed packet decomposition structure
  no block discontinuities
Inter-band borrowing in lifting steps is critical
 | LHH Power
Non oriented | 422.16
Oriented NO borrowing | 166.50
Oriented with borrowing | 4.73
 | HLH Power
Non oriented decomp | 423.07
Oriented No borrowing | 165.90
Oriented with borrowing | 4.59
LL
HL
LH
HH
LL
HLL
LHL
HH
HLH
LHH
(Mehrseresht & Taubman – ICIP 2006)
Related schemes, without borrowing:
(Ding, Wu, Li – PCS 2004) and (Chang & Girod – ICIP 2006)

## Slide 26: Geometry adaptive lifting – example
21
23
25
27
29
31
33
35
37
0.2
0.3
0.4
0.6
0.9
1.2
bpp
PSNR (dB)
Conventional Mallat
Oriented Mallat
Conventional PW
Oriented PW
PSNR of reconstructed Image
  5 levels of DWT
  Implemented as an extension to JPEG2000
  Orientation modeling uses quad-tree with R-D pruning but metric is not yet optimized
Reconstruction at equal PSNR

## Slide 27: Scalable video standardization – in JVT
Temporal transform (hierarchical B-frames)
Intra-prediction (intra-blocks only)
Spatial transform (DCT), quantize and encode
Temporal transform (hierarchical B-frames)
Intra-prediction (intra-blocks only)
Spatial transform (DCT), quantize and code
Motion prediction and coding
motion
motion
Spatial interpolation
Spatial interpolation
texture decode
Motion prediction and coding
texture decode
motion decode
motion decode
bit-stream
Temporal transform (hierarchical B-frames)
Intra-prediction (intra-blocks only)
motion
Spatial transform (DCT), quantize and code
Motion coding
H.264 + layered coding
H.264 + layered coding
H.264 + layered coding
Filter & decimate
Filter & decimate

## Slide 28: Scalable video standardization – status
Performance indicators:
  Can achieve roughly comparable performance to non-scalable H.264
    With careful encoder optimization!!
Lots of prediction (notionally open loop)
  Good adaptation of the prediction strengths in H.264
  But, remember that prediction alone is sub-optimal
What seems to be missing?
  extra lifting steps for noise shaping & reduction
  better adapted motion operators
  integrated spatial scalability

## Slide 29: Spatial aliasing – in wavelet transforms
Analysis filter responses of the
popular 9/7 wavelet transform
Fundamental constraint: (for perfect reconstruction)
half-band filter
0
0
1
Extract LL subband
Spatial aliasing

## Slide 30: Spatial pyramids – promising directions
reduce
expand
full res image
half res image
quantization
detail
base
expand
full res image
reduce
reduce
(Santa-Cruz, Reichel and Ziliani – ICIP 2005)
Prediction alone is sub-optimal!
31
32
33
34
35
400
600
800
1000
PSNR (dB)
kbits/s
single-level
LP-lift open loop
LP closed loop

## Slide 31: Spatial “wavelets” – promising directions
Modulated lifting steps (Gan and Taubman, submitted to ICASSP’07)

## Slide 32: Motion modeling – beyond quad-trees
Quad-trees are a natural mechanism for representing complex fields at variable density
Facilitate direct minimization of
  tree pruning
But, refinement creates a lot of redundant leaves
Leaf merging fixes things (De Forni & Taubman – ICIP 2005) (Tagliasacchi et al. – ICME 2006) inspired by (Shukla, Dragotti, Do & Vetterli – Trans IP 9/2005)

## Slide 33: Motion modeling – polynomial leaf merging
Extend models to allow translation & affine flow
  affine models derived by fitting regular MV’s
Initial R-D optimal tree pruning followed by a disciplined R-D driven leaf merging procedure
  no new exhaustive motion vector search is required
  single-pass, non-iterative scheme
(Mathew & Taubman – ICIP 2006)

## Slide 34: Distribution over lossy networks
Large body of work on on-line encoding with network feedback
  dynamic channel conditions used to modify encoding
  popular approach involves a stochastic frame buffer
    e.g., “Rope” (Zhang, Regunathan & Rose – JSAC, June 2000)
    Recent advances (Harmanci & Tekalp – Trans IP, to appear)
We focus here on scalably compressed media
  open loop coding
  protection dynamically applied to elements of the pre-encoded scalable bit-stream.
Packet erasure model is somewhat realistic
  ... each packet is correctly received or completely lost
  wired networks: congestion  packet losses
  wireless: bursty losses in deep fades  packet losses

## Slide 35: Priority Encoding Transmission (PET)
(Albanese, Blomer, Edmunds, Luby & Sudan – Trans IT, Nov 1996)
Each “frame” F[n] (or GOP, or subband frame, …)
  has a sequence of embedded (quality) elements:
Each is protected with a code selected from a family of (N,k) MDS codes, all with the same length N
So long as , whenever is decodable, so are
packet 1
packet 2
packet 3
packet 4
packet 5
redundancy index
r1=4
r2=3
r3=1
r4=0

## Slide 36: Protection assignment in PET
Lagrangian formulation:
  maximize:
    subject to:
  if source (Uq , Lq) characteristic is convex , and channel (Pr , Rr) characteristic is convex , can independently maximize each and the constraints will always hold.
[typically, U = -MSE]
(Puri & Ramchandran – Asilomar 1999) (Mohr, Riskin & Ladner – JSAC, June 2000)

## Slide 37: Limited Retransmission PET (LR-PET)
Each “frame” F[n] has two chances of transmission:
  primary at T[n]; secondary at T[n+]
Each transmission-slot T[n] sends source elements from
  current frame F[n]; and a previous (retransmitted) frame F[n-]
Transmitter knows number of packets k’, received in T[n-]
  Partial retransmission of element needed if
  During retransmission, effective length of is reduced
ACK[n]
Primary
Transmission
Secondary
Transmission
F[n]
F[n +1]
F[n +]
F[n ++1]
F[n]
F[n +1]
F[n -]
F[n - ]
T[n]
T[n +1]
T[n+]
T[n++1]

## Slide 38: Optimization over stochastic policies
In current transmission slot, server must decide:
  how to distribute bandwidth over primary & secondary frames
  how strongly to protect each primary & secondary element
Depends on the policy selected in the future
  How much bandwidth will be dedicated to retransmission?
    Depends on number of lost packets
Assume stationary protection assignment policy
  driven by stochastic packet loss process
    (Podolsky, Vetterli & McCanne – MMSP 1998)
    (Chou & Miao – submitted Trans. MM 2001)
    (Chou, Mohr, Wang and Mehrotra – DCC 2000)
primary
secondary
secondary
secondary
secondary
primary
primary
primary

## Slide 39: Optimization in LR-PET
Objective in slot T[n] is to maximize:
N+1 hypotheses on future retransmission, depending on the number of lost packets.
Regular PET optimization of redundancy indices for element retransmission.
Complexity: O (N log Q)
Complexity: O (N2 log Q)
execution time (msec per slot) on an old P4
0.5
0
150
50
N (packets per slot)
Q = 180 elements/frame
Plain PET
LR-PET
Frame
26
28
30
32
34
36
38
40
PSNR (dB)
1
6
11
16
21
26
LR-PET
Plain PET
Greedy LR-PET (without hypotheses)
(Taubman & Thie – Trans IP Aug 2005)

## Slide 40: LR-PET: extensions
Recent extensions: (e.g., Durigon & Taubman – ICIP06)
  unreliable acknowledgement
  stochastic delay (primary transmission might arrive after acknowledgement message sent to transmitter)
Same low complexity performance achieved also with these extensions, after some non-trivial manipulation
38
36
34
32
30
PSNR (dB)
PE
0.1
0.15
0.2
0.25
0.3
PET
PACK=1
PACK=0.75
PACK=0.5
Other directions:
  LR-PET with packet bit errors

## Slide 41: Client-server systems – accessibility
Model considered so far:
  Multi-dimensional transforms serve to:
    exploit redundancy (energy compaction)
    facilitate scalability – natural resolution hierarchies
  but, transforms interfere with accessibility
    e.g., access a region of a frame after MC temporal filtering
    need server to send us a lot more than we actually want
  Problem gets worse as we go to higher dimensions
    e.g., access a window at one time instant in multiview video
Scalable compression
Client (decompress)
media
Server
selects elements of interest
quality progressive delivery
protects content against loss
storage
channel

## Slide 42: Example from multiview imaging
If we want the whole lightfield
  efficiency greatly improved by a geometry compensated interview transform
If we want only one view
  better without the interview transform
Interactive navigation lies between these worlds
  slow navigation similar to the single view case
    better off with independently compressed images
  fast navigation similar to the whole lightfield case
    better off with a transform
  this has been demonstrated theoretically and practically by (Ramanathan & Girod – Image Communication, to appear)
f2
f0
Surface geometry (proxy)
f1

## Slide 43: An alternate approach
Server keeps original images
  scalable & accessible, but independently compressed
Server policy sends selective elements to the client
  depends on the client’s desired view, scale, region, …
  depends on content already in the client’s cache
    more on this shortly
Intelligent client combines available content
  redundancy exploited in the client
    motion/geometry compensation of existing cache contents from nearby views
Naturally open and extensible
  client can use whatever it has, to generate the best view it can
  new content (new views) can be added to the server any time
  client & server policies only weakly coupled
    dumb servers or dumb clients do not break anything

## Slide 44: Initial steps – client rendering problem
How it works:
Warping of the available views
Wavelet analysis
Distortion sensitive blending policy
Wavelet synthesis
(Zanuttigh, Brusco, Taubman & Cortelazzo – ICIP 2005)

## Slide 45: Initial steps – distortion sensitive blending
Scalable image compression
Geometry compression and modeling error
Lighting
Estimation of distortion for each sample in the source views
Accounting for different sources of distortion
Samples are chosen in order to minimize

## Slide 46: Initial steps – server optimization problem
Minimize the total distortion D* in the rendered views
Blending choices depend on the received data
Lagrangian optimization subject to bandwidth constraint
Distortion due to image compression
Distortion due to geometry and lighting
Blending choices
(Zanuttigh, Brusco, Taubman & Cortelazzo – MMSP 2006)

## Slide 47: Disruptive refinement
At first lower distortion achieved by exploiting existing cached data
  server may choose to refine this data, rather than sending closer views
Policy switching penalty associated with new (closer) views
Eventually disruptive refinement becomes favourable
  switching penalty changes effective R-D characteristic for new elements
policy switching penalty,
R-D curve ignoring
the client’s ability to exploit nearby views in its cache
Effective R-D curve,
accounting for policy switching penalty
First R-D
optimal switching point
First feasible
switching point

## Slide 48: One implication – loss of embedding
In scalable representations, lower qualities are always embedded within higher qualities
By constrast, if redundancy exploitation is based at the client,
  R-D optimal delivery involves both enhancing and disruptive (policy switching) refinements.
  Lower bit-rate services are not generally embedded inside higher bit-rate services

## Slide 49: Connections to distributed video
In distributed video coding
  some redundancy is exploited at the decoder
    e.g., motion-induced inter-frame redundancy
    viewed as a side-channel, available only at the decoder
  the encoder indirectly exploits the side channel
    (Wyner-Ziv coding)
    Approach 1: send coset indices of a suitable lattice quantizer (Puri & Ramchandran [PRISM] – Allerton 2002)
    Approach 2: send bits from a suitably punctured channel code (Aaron, Zhang & Girod – Asilomar 2002)
  advocated for low complexity encoding
    ME at decoder; encoder guesses side channel capacity
  these difficulties go away in the client/server scenario
    motion/geometry produced and stored during compression
    one (1st?) example of this: (Cheung, Wang & Ortega – VCIP 2006)

## Slide 50: Summary
Opening the loop in MC video coding
  enables efficient scalable coding
  prediction alone is sub-optimal
    but prediction alone has been sufficient for current standardization
  lifting steps can build reversible transforms along motion paths
Current and emerging work on new transforms
  motion/geometry adaptive, multi-resolution embedding, …
Efficient structures for protecting scalable content
  PET, LR-PET, … (hypotheses on future policy are the key!)
Accessibility is critical for interacting with massive media
  client side exploitation of redundancy may make the most sense
  strict embedding no longer holds in R-D optimal services
  distributed coding principles apply at the server

## Slide 51
Coogee Beach: 5 minutes from UNSW